## Slide 1
Update on hospital cleaning and disinfection (aka what’s lurking in your hospital room?)
Jon Otter, PhD FRCPath
Imperial College London
j.otter@imperial.ac.uk
@jonotter
Blog: www.ReflectionsIPC.com
You can download these slides from www.jonotter.net

## Slide 3: Transfer of a surrogate marker in a NICU
Oelberg et al. Pediatrics 2000;105:311-315.

## Slide 4: Transfer over time: inoculated pod

## Slide 5: Transfer of a surrogate marker in a NICU

## Slide 6
Your hospital room can make you sick!
Mitchell et al. J Hosp Infect 2015;91:211-217.

## Slide 7: Transmission routes
Otter et al. Infect Control Hosp Epidemiol 2011;32:687-699.

## Slide 8
86%
96%
58%
59%
93%
85%
French et al. J Hosp Infect 2004;57:31-37.
Notes: Survive for extended periods

## Slide 9: Surface survival
Organism | Survival time
Clostridium difficile (spores) | 5 months
Acinetobacter spp. | 3 days to 5 months
Enterococcus spp. including VRE | 5 days – 4 years (!)1
Pseudomonas aeruginosa | 6 hours – 16 months
Klebsiella spp. | 2 hours to > 30 months
Staphylococcus aureus, inc. MRSA | 7 days – 7 months
Norovirus (and feline calicivirus) | 8 hours to > 2 weeks2
SARS Coronavirus | 72 hours to >28 days3
Influenza | Hours to several days4
Adapted from Kramer et al. BMC Infect Dis 2006;6:130.
Wagenvoort et al. J Hosp Infect 2011;77:282-283.
Doultree et al. J Hosp Infect 1999;41:51-57.
Rabenau et al. Med Microbiol Immunol 2005;194:1-6.
Bean et al. J Infect Dis 1982;146:47-51.

## Slide 10: Terminal cleaning
Chart: 
Positive swabs | 90 | 66 | 72 | 1
(8 rooms; 2 four-bed bays previously occupied by MRSA patients)
Before cleaning
After cleaning
Percentage of MRSA swabs positive
French et al. J Hosp Infect 2004;57:31-37.
26% reduction
90% of 124 sites
66% of 124 sites

## Slide 11: Surface -> Hand -> Patient
Pathogens can be transferred from surfaces to HCW hands without direct patient contact1-2
Boyce et al. Infect Control Hosp Epidemiol 1997;18:622-627.
Bhalla et al. Infect Cont Hosp Epidemiol 2004;25:164-167.
Hayden et al. Infect Control Hosp Epidemiol 2008;29:149-154.
Stiefel et al. Infect Control Hosp Epidemiol 2011;32:185-187.
Guerrero et al. Am J Infect Control 2012;40:556-558.
Randle et al. J Hosp Infect 2010;76:252-255.
52% of 23 HCW acquired VRE on their hands3 | Contact with patient or surface = ~10% risk of acquiring VRE3
45% of 50 HCW acquired MRSA on their hands4 | 40% of 50 HCW acquired MRSA on their hands4
50% of 30 HCW acquired C. difficile on their hands5 | 50% of 30 HCW acquired C. difficile on their hands5
Compliance with hand hygiene: 50%6 | Compliance with hand hygiene: 80%6

## Slide 12
Chased by an antibiotic-induced C.difficile-shaped shadow!
Freedberg et al. JAMA Intern Med 2016;176:1801-1808.
Significant risk factors for CDI.

## Slide 13: Rethinking the ‘inanimate’ environment
Scanning electron microscopy identified biofilm on 5/6 dry hospital surfaces from an Australian ICU (including MRSA on 3/5).1
Followup study identified biofilm on 41/44 (93%) of surfaces in an ICU; MRSA from 18%, ESBL from 11% and VRE from 8% of the samples.2
1. Vickery et al. J Hosp Infect 2012;80:52-55.
2. Hu et al. J Hosp Infect 2015;91:35-44.
Could explain why vegetative bacteria can survive on dry hospital surfaces for so long
Be part of the reason why they are so difficult to remove or inactivate using disinfectants
Explain (to some degree) the difficulty in recovering environmental pathogens by surface sampling

## Slide 14: Can we modify the ‘environmentome’
Vandini et al. PLoS ONE 2014;26;9(9):e108598.
More here if you’re interested.
Bacterial load of coliforms (black circles) and S. aureus (white circles). Black arrow = beginning of the “live” cleaning agent; black dotted arrow = conventional cleaning agent.

## Slide 15: Could spore soup out compete AMR?
Caselli et al. PLoS ONE 2016;11:e0148857.
Impact of Bacillus-based cleaning on the antibiotic R genes of the contaminant microbiota of hospital surfaces.

## Slide 16: “It’s airborne”
Best et al. Clin Infect Dis 2010; 50: 1450-7.
Detection of C. difficile in the air samples from the rooms of 50 patients.
Chart: % sites contaminated
| Symptomatic | Asymptomatic
% sites contaminated | 10 | 2

## Slide 17: “It’s airborne”
Results of intensive air sampling surrounding 10 patients. C. difficile was detected in the air in 7/10 patients.

## Slide 18
Improve existing procedures
Try something new!

## Slide 19: Contamination-sparing therapy?
n = 66 patients (rooms) and 264 surfaces for vancomycin / metronidazole, and 68 patients (rooms) and 272 surfaces for fidaxomycin. p<0.05 for both rooms and surfaces.
Biswas et al. J Hosp Infect 2015;90:267-270
Chart: % contaminated with C. difficile
| Vancomycin / metronidazole | Fidaxomicin | Vancomycin / metronidazole | Fidaxomicin | Rooms | Sites in rooms
% contaminated | 57 | 37 | 27 | 17

## Slide 20: Antimicrobial surfaces (e.g. copper)
Salgado et al. Infect Control Hosp Epidemiol 2013;34:479-486.
Chart: % patients who acquired
| Non copper | Copper
HAI or MRSA / VRE colonisation | 12.8125 | 7.1429
HAI only | 8.125 | 3.4014
Bedrails
Overbed tables
IV poles
Visitor chair arms
Nurse call button*
Computer mouse*
Computer palm rest*
Rim of monitor*
(* = some rooms only)
-44%
p=0.020
-58%
p=0.013
614 pts in 3 hospitals randomised to ‘copper’ or ‘non-copper’ ICU rooms

## Slide 21: Control contamination at the source
Chart: 
| Acquisition rate (per 1000 at-risk patient days) | Environmental contamination (% sites contaminated)
Control period | 44 | 30
Intervention period | 21 | 10
Chung et al. Am J Infect Control 2015;43:1171-1177.
Pre-post study in a 16-bed ICU in Korea; CHG daily bathing implemented for 12 months after 14-month pre-intervention period. Significant reduction in rate of carbapenem-resistant Acinetobacter baumannii acquisition and environmental contamination.

## Slide 22
Improve existing procedures
Try something new!

## Slide 23: Wiping away infection
Orenstein et al. Infect Control Hosp Epidemiol 2011;34:521-523.
2.4
cases / 1000 patient days
0.4
cases / 1000 patient days
Impact of changing from QAC to bleach wipes for daily disinfection of all rooms. Cleaning thoroughness was 97-98% throughout the study using ATP benchmarking (<250 RLUs).

## Slide 24
Cleaning / disinfection failure
External
Product
Procedure

## Slide 25
‘Given the choice of improving technology or improving human behavior, technology is the better choice’.
Dr Bob Weinstein
Weinstein RA. Emerg Infect Dis 1998;4:416-420.

## Slide 26: Automated room decontamination (ARD)
Hydrogen peroxide vapour
30% H2O2 (HPV)
Aerosolised hydrogen peroxide 5-6% H2O2 (AHP)
Ultraviolet radiation (UVC)
Pulsed-xenon UV (PX-UV)
Otter et al. J Hosp Infect 2013;83:1-13.

## Slide 27: ARD systems - overview
Otter et al. J Hosp Infect 2013;83:1-13.
 | HPV 30-35% H2O2 vapour | AHP 5-6% H2O2 + Ag aerosol | UVC UVC (280 nm) | PX-UV Pulsed-xenon UV
Efficacy | 1 >6-log reduction | 2 ~4-log reduction | 3 ~2-4 log reduction | 4 ~1-3 log reduction
Distribution | 1 Homogeneous | 2 Non-homogenous | 3 Line of sight issues | 3 Line of sight issues
Ease of use | 4 Multiple units; sealing / monitoring | 3 Sealing & monitoring | 2 Multiple positions; no sealing / monitoring | 2 Multiple positions; no sealing / monitoring
Cycle time | 3 ~1.5 hrs single room | 4 >2 hrs single room | 1 ~10-30 mins | 1 ~10-30 mins
Purchase cost | 2 | 1 | 3 | 3
Running cost | 4 | 3 | 1 | 1

## Slide 28
Persistent contamination – sorted!
Chart: % sites contaminated
| 2 x bleach disinfection | 4 x bleach disinfection | Bioquell
% sites contaminated with A. baumannii | 12.1 | 1.8 | 0.2
% sites contaminated with MRSA | 3.6 | 1.9 | 0.1
Manian et al. Infect Control Hosp Epidemiol 2011;32:667-672.
140 samples from 9 rooms after 2xbleach
5705 samples from 312 rooms after 4xbleach
2680 sites from 134 rooms after HPV
HPV

## Slide 29: HPV: clinical impact
Passaretti et al. Clin Infect Dis 2013;56:27-35.
Chart: Rate / 1000 patient days
 | 10.6 | 4.1
64% reduction in the rate of MDRO acquisition
Standard cleaning / disinfection
HPV decontamination
30-month prospective cohort intervention study performed on 6 high-risk units (5 ICUs) including 8813 patients at Johns Hopkins Hospital.

## Slide 30: HPV: clinical impact
McCord et al. J Hosp Infect 2016.
2 years before HPV, 2 years during HPV. Breakpoint model indicated significant reduction in rate of CDI when HPV implemented (1.0 to 0.4 per 1000 patient days, 60% reduction).

## Slide 31
Anderson et al. Lancet 2017;389:805-814.
Cluster randomised study over >2 years across 9 hospitals including >25,000 exposed patients (admitted into a room where the previous occupant was known to have an MDRO). * = statistically significant reduction in the per-protocol analysis. ** = statistically significant when rooms occupied by patients with C. difficile removed from the analysis.
UVC: clinical impact
Chart: Rate / 10,000 exposure days
| C. difficile | MRSA | VRE | All target organisms
QAC | 50.3 | 63.4 | 51.3
UV | 36.5 | 29.4 | 33.9
Bleach | 31.6 | 48.2 | 31.9 | 41.6
Bleach + UV | 30.4 | 46.9 | 39 | 45.6
*
*
*
*
**

## Slide 32
Improve existing procedures
Try something new!

## Slide 33
Try something new!
“Design bugs out!”
Design Bugs Out – Product Evaluation Report. The Healthcare Associated Infection Technology Innovation Programme. UK Department of Health. 2011.

## Slide 34
ECDC Point Prevalence Survey of healthcare-associated infections and antimicrobial use in acute care hospitals (HAI-Net PPS) in the period 2011-2012 as reported to TESSy as of 2013-02-06 14:06:48
Try something new!
Single room shortage

## Slide 35: ‘Privatization’ of an ICU
Teltsch et al. Arch Intern Med 2011;171:32-38.
Intervention
24 bed ICU
2x10 bed and 4xsingle rooms
Converted to 100% single rooms in 2002
Comparison
25 bed ICU
2, 5, 6 or 8 bed rooms
No change in unit configuration
Change in the acquisition rate ratio before and after privatisation; * = not statistically significant.
Chart: % reduction in acquisition
| C. difficile | MRSA | Acinetobacter | Stenotrophomonas | Coag neg staph
% reduction | -43 | -47 | -53 | -52 | -4
*
*
Try something new!

## Slide 36: Reducing missed isolation days
Pathogen | Pre-pod use |  |  | During pod use |  |  | p value
 | n missed isolation days | Total required isolation days | % isolation days missed | n missed isolation days | Total required isolation days | % isolation days missed | 
MRSA | 303 | 591 | 51.3 | 33 | 410 | 8.0 | <0.001
ESBL / CRE | 149 | 565 | 26.4 | 118 | 750 | 15.7 | <0.001
Respiratory viruses | 108 | 179 | 60.3 | 38 | 233 | 16.3 | <0.001
Rotavirus | 68 | 138 | 49.3 | 45 | 74 | 60.8 | 0.109
Overall | 662 | 1138 | 58.2 | 205 | 1382 | 14.8 | <0.001
Keward et al. J Infect Prevent in press.

## Slide 37
Improve existing procedures
Try something new!

## Slide 38
Update on hospital cleaning and disinfection (aka what’s lurking in your hospital room?)
Jon Otter, PhD FRCPath
Imperial College London
j.otter@imperial.ac.uk
@jonotter
Blog: www.ReflectionsIPC.com
You can download these slides from www.jonotter.net